#### Trials and Tribulations
@@@@@@@@@@@@Image

From the image above you can see 6 different iterations of this quadcopter design.
From the top left to the bottom right you can see the change in materials and design modifications.

This is by no means a comprehensive list of different iterations. This is just what I found lying around at home. The following are some of the design considerations.

### Materials
I have been experimenting with many different materials, my primary concerns are weight, flexibility/rigidity and strength.

At first I experimented with Acrylic at first which is really easy to lasercut and I have access to a laser cutter, so for my purposes this was the best material to prototype with. Acrylic is quite expensive compared with other materials such as Polycarbonate or plywood but my main issue was it was so brittle. I have had many light crashes where the frame just snapped in two. This not being my first quad, I am very used to crashes and having them break but these frames need to be more resilient, this was unacceptable.

******IMAGE

I next tried polycarbonate, this material is used in bullet-proof glass. It is heavier than acrylic and also surprisingly flexible I could bend it back on itself.

@@@@@@@@@@@@@@@@@@@@@@@@PIC@@@@@@@@@@@@@@

This material also had to be water-jet cut as laser-cutting caused all sorts of toxic fumes to come out, and this process is so much more costly.

In my search I started to look at different types of plywoods. I first had started on marine ply which is very toxic to lasercut but readily available. Marine Ply is quite heavy, very strong and waterproof. It was however too heavy for my applications but was very interesting to play around with.
While looking at ply I came across bamboo ply which fulfils most of my criteria. Its very light, cheap and quite strong. This is what I have been designing with more recently and its been very nice to work with. The strength is not as good as I would have liked and I have had to reinforce it in places to make sure it does not snap.
*********Image of snapped Bamboo ply

## Weight vs Flexibility/Rigidity

Weight is the most crucial design consideration as it effects the flight characteristics. If its too heavy it won’t be able to take off or reduce your flight time. There is a polynomial relationship between the weight and your flight time.

Flexibility is important in quadcopter design because it needs to be able to absorb impact such as crashes or hard landings. Some crashes will be fatal no matter how good the design is. Impacts happen all the time and can be mitigated by good landing legs and the frame being designed to absorb the impact. You want to have some flex so the frame as a whole absorbs the impacts and this will also reduce vibration issues.

Acrylic was a good example of this, every time I landed even lightly it would crack or shatter the frame. This could not be mitigated by legs because the material was just too brittle and did not have enough flex.

### Material Properties in Summary

Acrylic
- Light
- Cheapish
- Brittle
Polycarbonate
- Heavier than acrylic
- incredibly strong
- cheaper that acrylic
- too flexible at 3mm thickness
Plywood
- Strong
- Cheap
- Heavier that Acrylic
Bamboo Ply
- Light
- Strong but not as strong as normal plywood, needs to be reinforced
- more flexible than Acrylic
- bit more expensive than normal plywood

Carbon fibre – Ideal for quadcopter frames light, strong but so hard to cut and very expensive. It has a tendency to shatter and send shards everywhere.
- Light
- Strong
- Expensive
- Hard to cut
- on crashing shatters really badly.

## Conclusion

I hope that has given quick overview of design considerations going into building a quadcopter and rapid prototyping.

New blog

### Design Issues

--Issues with cracking and spliting due to holes and cracking due to acylcy

--Making tihicker area around holes

--rounded eddges for coners as they are a point of snapping.

--shrinking the arms so to increase of coverage of air flow.

--working the materials short falls.

--Wire routing

Power compass compensation

Raspbery Pi + Navio+ = Autonomous rover.

@@@@@@ PHOTO Of rover

# Why?

So I had this remote control car lying around my house and had recently bought the Navio+ flight controller for controlling a quadcopter. After playing around with this flight controller for a while I realised it would take a large amount of work to adapt it to my larger quadcopter. So I decided to mount and test it out on the car. Since its using the Ardupilot (http://ardupilot.com/) a fully featured UAV platform; it has heaps of support including phone apps to control it. I was excited about the Navio+ platform because it is built on the Raspberry PI. This means it can do more than just controlling the vehicle. The Raspberry PI has a quadcore CPU and heaps of ram and runs linux. This means I can do sensor processing on the car instead of having to communicate with a laptop.
This means that it could do object recognition and camera based collision avoidance on the car.

### BOM (not including shipping)

# The Car http://www.hobbyking.com/hobbyking/store/__23465__1_10_Quanum_Skull_Crusher_2WD_Brushless_Monster_Truck_ARR_.html
AUD $183.82

## Navio+ Flight Controller, GPS antenna, Wirepack and power module. USD $213 http://www.emlid.com/

#Pi 2+ $35 USD http://www.element14.com/community/community/raspberry-pi/raspberrypi2

#WiFi dongle TP-Link TL-WN722N- AUD$18 Don’t just use any wifi dongle, make sure its compatible with the PI.

#RC controller make sure the receiver outputs CPPM as this is the only format supported by the Navio++. I use the FrSky Taranis+ with a D8R-XP receiver as this is what I had at home. This setup costs around AU$37 for the recivert and the transmitter costs about $300.

# Xbee modules. (Optional)

## Setting up autostartup

## Wiring up.

##Compiling Ardupliot on the PI

Instructions on how to update the gcc and g++ versions on the PI 2+
https://somewideopenspace.wordpress.com/2014/02/28/gcc-4-8-on-raspberry-pi-wheezy/

This needs to be done as the https://github.com/diydrones/ardupilot build requires later versions of gcc to build correctly.

You will also need to remap the make file to use the local gcc not the crossed complied version.
I forgot to add you will also need to change the /mk/find_tools.mk and find the navio lines.

Toolchains for Raspberry Pi

RPI_CXX := arm-linux-gnueabihf-g++
RPI_CC := arm-linux-gnueabihf-gcc
RPI_AS := arm-linux-gnueabihf-gcc
RPI_AR := arm-linux-gnueabihf-ar
RPI_LD := arm-linux-gnueabihf-g++
RPI_GDB := arm-linux-gnueabihf-gdb
RPI_OBJCOPY := arm-linux-gnueabihf-obj

and change it to

Toolchains for Raspberry Pi
RPI_CXX := g++
RPI_CC := gcc
RPI_AS := gcc
RPI_AR := ar
RPI_LD := g++
RPI_GDB := gdb
RPI_OBJCOPY := obj

## Setting up the Autostartup for Ardupilot

 #settings http://rover.ardupilot.com/wiki/tuning-steering-and-navigation-for-a-rover/